# SP3 – HDMI Notes (2)

# 21-Feb-2014,

# Stan Bleszynski, Bryston Ltd.

HDMI Output Controls

(applicable to firmware revision 2014.02g or later)

Table1. Behavior of SP3 HDMI Outputs (2 parallel sockets (*))

| MISC-->HDMI Input | =SOURCE | =SOURCE | STICKY | STICKY |
| --- | --- | --- | --- | --- |
| OTHER-->DIGI OUT | ZDAC | Opti (Toslink) | ZDAC | Opti (Toslink) |
| MISC-->HDMI A-Out |  |  |  |  |
| MUTED | Video pass-thru, audio muted | Video pass-thru, audio muted | Video pass-thru, audio muted | Video pass-thru, audio muted |
| 2Ch Downmix | Video pass-thru, audio = 2ch downmix of the current main HDMI, SPDIF or analog input. Audio is muted in Bypass. | Video pass-thru, audio muted. | Current src is non-HDMI: video and audio pass-thru the last active HDMI source. Current src is HDMI: vide pass-thru, audio = 2ch downmix | Video pass-thru, audio muted. |
| 8Ch Bypass | Video and audio pass-thru (2-8channels) | Video and audio pass-thru (2-8channels) | Last active or currently active video and audio pass-thru (2-8channels) | Last active or currently active video and audio pass-thru (2-8channels) |

Note (*):	HDMI subsystem firmware revision "00001026" or earlier, see SYSTEM SETUP-->TEST-->SYSTEM STATUS,  handshakes the stream format to be the lowest denominator of the two active "Sink" devices connected to HDMI Out1 and Out2 sockets.  For example, if two different TV screens are connected and powered, the lowest video  resolution of the two will be played!   If the highest resolution is required, unplug the lower screen and reselect HDMI source to re-handshake!