# SP3 – HDMI Notes (3)

# 22-Oct-2013,

# Stan Bleszynski, Bryston Ltd.

HDMI Startup Options

(applicable to firmware revision 2012.12 or later)

SOURCE SETUP-->OTHER-->HDMI STARTUP   (source specific option)

- If playing does not resume automatically after switching away and back to an HDMI source, setting of this parameter a value other then AUTO may help.  This parameter can be set on a per-source basis depending whether a particular HDMI device may need it.

Not all players need it, many if not most work very well with the default setting of 0 AUTO.

There are 3 settings for HDMI STARTUP

0 AUTO     - default behavior, works with most players and sources.  Clock pullup termination is enabled only for an active input.   EDID is re-handshaked only on startup or plug-in.

1 EDID       - forces re-sending EDID (part of HDMI handshake protocol, device description) each time HDMI source  is switched.  It slows down reconnection slightly but it makes re-start more robust if a player tends to default  itself to a lower format,  when the HDMI link is switched away from it.

2 KEEPON - keeps HDMI clock line pulled up enabled even if an HDMI input is inactive (unselected), to force ("fool")  the player to maintain a connection alive.  It speeds up re-activation of this input when it is reselected, but it may cause side effects or cause error messages with some players.

1 & 2 - both of the above options EDID and KEEPON are applied.

Note:

- Some minority of the players may need 1 or 2, some may need 1&2, otherwise they exhibit  lack of audio sync after switching the source.  Most of the Blueray players that have been tested so far work reliably with the default setting of 0 AUTO.