Board HSR72Q Specifications.

(updated 26-April-2018)

HDMI inputs # 4 through #7 are HDMI 2.0b and HDCP 2.2 compliant, 18Gbps (aka 6G, 600MHz)

·       ALL commercially available formats can be properly passed to Output #2

·       4K-24/30 Hz, 4.4.4, 8-12 Bit

·       4K-24/30 Hz, 4.2.2, 8-12 Bit

·       4K-50/60 Hz, 4.4.4, 8-Bit

·       4K-50/60 Hz, 4.2.2, 8-12 Bit

·       4K-50/60 Hz, 4.2.0, 8-12 Bit

·       Support for BT.2020 color space, at all above resolutions

·       Support for HDR-10, including “UHD Premium” designated content

Output #2 (to the right, when viewed from the rear) must be used for HDMI 2.0b.

Output #1 is HDMI 1.4a and should in general not be connected for proper results from output #2.

HDMI inputs #1 through #3 are programmed as HDMI 1.4a for compatibility reasons, because

some legacy devices are not backwards-compatible with anyone’s HDMI 2.0b inputs.

Use these inputs for legacy 1080P sources or Audio Only outputs.