# SP3 -  RS232 port

(09-Jan-2012, Stan B., Bryston Ltd.)

## How to enable RS232 port

RS232 parameters can be set in the hidden screen.  under Miscellaneous.  The communication format is fixed: 8 bit data, 1 start bit,1 stop bit, no parity, no handshake.

There are two configurable parameters:

1) RS232 MODE: OFF/ON/ON+AUTOFB

OFF - RS232 port is disabled

ON   - RS232 port is ON without auto-feedback

ON+AUTOFB   - RS232 port is ON with auto-feedback

2) RS232 BAUD:  9600/19200/38400

- baudrate selection (default is 9600)

## Connector diagram

Testing of SP3 communication.

The following free RS232 terminal utilities can be used for testing the SP3 communication:

Termite 2.7 (tested OK, easy and straightforward to use):

http://www.compuphase.com/software_termite.htm

Hercules 3.2.4 (tested OK, type commands as ##10MSRC03<CR>, no local echo, can use TCP/IP)

http://www.hw-group.com/products/hercules/index_en.html

Other free (untested):

http://download.cnet.com/Ckubed-Advanced-Terminal-Program/3640-2085_4-10234733.html

(note: I used and tested an old version 2 of CKubed on WinXP, however seem to be problems with uninstalling of the current version 4.4)

http://realterm.sourceforge.net/index.html#downloads_Download

Sources for MS VB.net and C#:

http://www.lvr.com/files/com_port_terminal_vb.zip

http://www.lvr.com/files/com_port_terminal_cs.zip

# Footnotes

To unlock the hidden screens: go to Miscellaneous, scroll down to the bottom screen (3-rd from the top).  Press ZONE,DVD and TAPE buttons, one at a time, in this order.  A down arrow will appear in the bottom right corner of the screen.  Scroll down until you see the required parameter.

RS232 commands sent will still be echoed back using standard reply format described in the helpcmd.txt

Autofeedback is the response similar to an RS232 command response described in helpcmd.txt but issued by the SP3 to Host following a system status change, initiated by non-RS232 action.  For example, when DVD front panel button is pressed SP3 would send #10MSRC00<CR> back to host.