# SP3 – User’s Instructions for USB

# (31-July-2012, Stan B., Bryston Ltd.)

USB port (Revision 1.1) in the SP3 emulates the streaming receiver device. It allows receiving a digital sound stream from a host device such as a PC, originating from a file or internet, and playing it through SP3 audio processor.

Initiating a USB connection with a PC (Windows 7).

Make sure SP3 is connected to a power source but in Standby.  When the USB cable connecting SP3 is plugged to a USB port in a PC and SP3 is taken out of Standby, a message Driver Software Installation is produced in the system tray area.  Clicking on it opens up the following message window:

Message screen on USB connection event.

Device Manager window (Control Panel).

See BRYSTON SP3 item under “Sound, video and game controllers” section.   If this is not present as illustrated above, then the SP3 USB port is not connected or not recognized by the operating sustyem.

Selecting “BRYSTON SP3” as the default Audio Device.

Sound Manager window (from the System Tray)

Click on the “Speakers/BRYSTON SP3” line to make this the default.

When BRYSTON SP3 has been selected as the default speaker, then any media player device will be outputting digital audio stream through the USB port to SP3.

To test the operation,  press USB button on the SP3 front panel and start Windows Media Player, then select and click one of the sample music files.

Configuring MAC OS for USB streaming to SP3.

The idea is the same as in Windows, that is Bryston SP3 has to be selected as the output audio device.  The following screenshots illustrate the necessary steps:

Step 1 - In Utilities select Applications, then Audio MIDI Setup

Step 2 - Select BRYSTON SP3 and "Use this device..."