# SP3 Web Interface Guide

# 2-Aug-2012, Stan Bleszynski,  Bryston Ltd.

1. General guidelines (introduction).

SP3 can be connected to a PC (Windows, MacOS, Linux etc) using Ethernet cable through a local area network hub or through a direct peer-to-peer (SP3-to-PC) using a cross-over network cable.  Connection between SP3 and a PC can be established using either one of the 3 basic configuration schemes differing in the way the IP addresses are leased out or assigned by an external or internal DHCP server.   This is described in more details in the following document on-line:

ftp://ftp.bryston.com/pub/firmware/sp3/doc/SP3_setup_using_LAN2.doc

2. Main screen.

Communication interface with the SP3 takes place over TCP/IP stack using HTTP (version 2 compat) protocol over port 80.  This can be handled by almost any internet browser, for example Internet Explorer, Chrome, Safari, Firefox, Opera, and on any operating system platform.    Once a connection is established, so-called “Net Bios Name” of the SP3, or its IP address in the browser URL window and pressing enter, should bring on the following screen:

Main SP3 web interface screen

2. File upload screen.

Click on the top “File” menu link on the main SP3 web interface screen brings the “Firmware Upload” screen.

All SP3 screens except Main and Help require a password.   The first time File is clicked on the Main screen, an intermediate password entry screen will show up:

Firmware Upload screen

Insert the user name admin and password bryston as shown above and click OK button.  Once this is done, it is valid for as long as the browser is not exited and the user will not have to re-enter it again.

Firmware Upload screen

Clicking on the “Upload Image File (.bin) opens up a file selection subscreen which allows selecting a compressed firmware file (of type .bin) and then starting upload and programming.  This is described in more details in the following on-line document:

ftp://bryston.com/pub/firmware/sp3/doc/SP3_Firmware_Upload_Instructions.doc

Note: selecting of “Restricted Default Flash Partition” allows overwriting of backup files in the SP3 flash.  This option is normally not enabled and a special password would be required.

3. Setup screen.

Setup screen

This screen displays network-connectivity settings and also allows modification of:   DHCP mode selection, IP address, Gateway IP address, Subnet Mask, Primary DNS and Secondary DNS.

MAC Address and Host Name are hardcoded and cannot be changed and saved!

4. Status screen.

Setup screen (as of firmware version 2012.04)

Status screen displays the current “Error and Status messages” (if any), and “Number of Flash Write Cycles”.

Note: the following error "PWRGD PWR Stat Fail" or "Power or fuse failed" typically comes accompanied by other secondary messages such as "Volume Control Fault", "DSP Fault after Reset", "Invalid Alpha Reply", "DSP Fault" etc.  It is most likely caused by a blown fuse.  To replace the fuse, locate it in the far left corner inside the unit, after opening up the top cover.

5. Help screen.

Help screen as of  release 2012.04  (top part)

The top part of the Help screen contains 3 important links to documents:

User Manual – an on-line version of the user manual (this link requires an active Internet connection to work)

Remote Communication Commands – displays the list of available RS232 commands, such as #10MPWR01 etc.

Infrared Remote Control Codes - displays the list of available IR remote controller codes.  The codes can be entered in to BR3 remote controller by pressing “Code” button once (which lights the red LED) and then pressing three numeric buttons in the short succession while the red LED is lit.

Note: some of the help hyperlinks point to embedded files in the SP3, while some other, such as the user manual, point on-line thus require active  internet connection.

Help screen (bottom part)

# Footnotes

In the new firmware revision (from 2012.08+), an alternative user name of  bryston with the same password bryston, will also be accepted

This page is currently obsolete and will be expanded in the future software revisions to allow complete system configuration.

This is the same as “Net Bios Name” referred elsewhere in the documentation.

This screen will be modified in the future to display information available currently on the SP3 Vacuum Fluorescent display in menus SYSTEM SETUP(TEST(SYSTEM STATUS and HDMI STATUS.

This is an advanced technical information of no relevance, used only for  diagnostics and  support.

Numeric buttons 0-9 in the BR3 are assigned to the following buttons, in this order:  MUTE=0, TEST=1, DTS=2, DOLBY=3, 2CH=4, HDMI=5, DIG=6,  (SURR=7, SURR(=8, STEREO=9.