SP3 BRYSTON SERIAL PROTOCOL

13-April-20165   Stan Bleszynski   Bryston Ltd.

SP3 can receive commands and can send responses to each command.  It can also (optionally) broadcast automatic responses to certain system events such as source switching from the front panel etc. (see AUFB).   The following commands can be sent over RS232, RS485 (with a RS232/RS485 interface) and TCP/IP (using GET mechanism over port 80).

Command format:

RS232: ASCII string beginning with # ending with carriage return  (ASCII code 13).

| # | D1 | D2 | C1 | C2 | C3 | C4 | P1 | P2 | ... | <CR> |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| # | command start character (TCP/IP: use URL code %23) |
| --- | --- |
| D1 | device category, one digit 1..f (for SP3 D1 must be 1) |
| D2 | RS485 device ID, 1 digit 0..f(dflt=0). D2=0 typically and can only be changed through the front panel menu! |
| C1..C4 | command name (4 chars) , typically uppercase ASCII letters. |
| P1,P2 | parameters are two or more arbitrary ASCII characters. |
| <CR> | Carriage return end char, code 13 (TCP/IP: use dot ‘.’) |

Example of power up command (RS232):

#10MPWR01<CR>

Example of power up command (TCP/IP):

%2310MPWR01.

Response format:

Response format is the same as commands,  repeating the D1,D2,C and P bytes (P bytes may carry 	either an actual status value or ?? in case of errors).

Example:

#10MPWRQS<CR>	( command: query power status

#10MPWR00<CR>	( response:  power is off (in standby)

#10MPWR01<CR>	( command: power up

#10MPWR01<CR>	( response(delayed):  power is on

Notes:

All characters preceding the # of a command, and following the <CR> will be ignored.  Do not insert #,  spaces, <LF>, <TAB> or other non-ASCII characters inside the command string.

When using TCP/IP, replace carriage return character with the dot ‘.’ character.

Do not assume that the number of response bytes R1,R2,… is always fixed.  Allow up to 320 bytes to be read or until a <CR> is encountered.

The format of the automatic responses is the same as the response to a serial command sent with the parameter bytes P1 P2 = "QS".

All commands except MPWR and INFO are ignored in standby.

| COMMAND NAME | PARAM. | DESCRIPTION |  | COMMAND NAME | PARAM. | DESCRIPTION |
| --- | --- | --- | --- | --- | --- | --- |
| MPWR |  | Set Main Power (works in standby!) |  | DVOL |  | Dolby Volume (DV) or Dynamic Range Compression (DRC) enable/disable |
|  | 00 | Off (Standby) |  |  |  |  |
|  | 01 | On |  |  | 00 | All OFF |
|  | QS | Query Status |  |  | 01 | Dolby Vol on , DRC off |
|  |  |  |  |  | 02 | -- |
| MSRC |  | Set Main Source |  |  | 03 | -- |
|  | 00 | DVD |  |  | 04 | -- |
|  | 01 | SAT |  |  | 05 | -- |
|  | 02 | TUNER |  |  | 06 | -- |
|  | 03 | CD |  |  | 07 | DRC LINE (medium), DV off |
|  | 04 | DVR |  |  | 08 | DRC RF (strong), DV off |
|  | 05 | TAPE |  |  | 09 | DRC AUTO (only Dd THD & DTS-HD) , DV off |
|  | 06 | BAL1 |  |  | QS | Query Status |
|  | 07 | BAL2 |  |  |  |  |
|  | 08 | USB |  | DDVL |  | Dolby Volume Adjust |
|  | 09 | 7.1 Bypass |  |  | xxxx | 0200..1120 |
|  | QS | Query Status |  |  |  | (-80.0..12.0dB) |
|  |  |  |  |  |  | Set DV Calib. Offset (default=0) |
| MVOL |  | Set Main Volume |  |  |  | (High value = less loud!) |
|  | UP | Up 1 step (quick) |  |  | MSm | m=0,1 Reserved (mid/side is always off) |
|  | DN | Down 1 step (quick) |  |  | LVa | Leveler a=0=off, 1=Low, 2=Medium, 3=High |
|  | xxxx | 0200..1120 in 0.1dB |  |  | HMh | Half Mode h=0=off, 1=on |
|  |  | units plus 1000 |  |  | QS | Query Status, returns: |
|  |  | Range -80.0..+12.0dB |  |  |  | DDVLxxxxMSmLVaHMh |
|  |  | Resol. 0.5dB slow ramp |  |  |  |  |
|  | QS | Query Status |  |  |  |  |
|  |  |  |  |  | QS | Query Status DDVLxxxxMS1 |
|  |  |  |  | TEST |  | Pink noise setup |
| MMUT |  | Set Main Mute |  |  | ALL | Automatically sequence |
|  | 00 | Mute Off |  |  |  | all channels every 4s, |
|  | 01 | Mute On |  |  |  | then exit. |
|  | 02 | Mute toggle |  |  | MAN | Start manual sequence |
|  | QS | Query Status |  |  |  | or increment channel if |
|  |  |  |  |  |  | already started |
| ZSRC |  | Set Zone Source |  |  | LF | Start Left front (01) |
|  | 00 | DVD |  |  | CN | Start Centre (02) |
|  | 01 | SAT |  |  | RF | Start Right front (03) |
|  | 02 | TUNER |  |  | RS | Start Right surround(04) |
|  | 03 | CD |  |  | RB | Start Right back (05) |
|  | 04 | DVR |  |  | LB | Start Left back (06) |
|  | 05 | TAPE |  |  | LS | Start Left surround (07) |
|  | 08 | Digital Downmix |  |  | SB | Start Subwoofer (08) |
|  | QS | Query Status |  |  | EX | Stop and Exit pink |
|  |  |  |  |  |  | noise setup |
| ZVOL |  | Set Zone Volume |  |  | QS | query status. Resp |
|  | UP | Up 1 step (quick) |  |  |  | 00 = not playing |
|  | DN | Down 1 step (quick) |  |  |  | 01 = L (left front) |
|  | xxxx | 0200..1120 (slow ramp) |  |  |  | 02 = C (center) |
|  |  | Range -80.0..+12.0dB |  |  |  | 03 = R (right front) |
|  | QS | Query Status |  |  |  | 04 = Rs (right surr side) |
|  |  |  |  |  |  | 05 = Rb (right surr back) |
| ZMUT |  | Set Zone Mute |  |  |  | 06 = Lb (left surr back) |
|  | 00 | Mute Off |  |  |  | 07 = Ls (left surr side) |
|  | 01 | Mute On |  |  |  | 08 = SUBWOOFER |
|  | 02 | Mute toggle |  |  |  |  |
|  | QS | Query Status |  | INPT |  | Query Input Signal |
|  |  |  |  |  |  | (Source Program) |
| MENU |  | Menu |  |  | QS | query, response xx= |
|  | LE | Left |  |  |  | 00: Unknown or not playing |
|  | RI | Right |  |  |  | 01: Analog, BP7 or BP2 |
|  | UP | Up |  |  |  | 02: Digital pass-through |
|  | DN | Down |  |  |  | 03: Pink-noise test |
|  | INC | Increment parameter |  |  |  | 04: Auto |
|  | EX | Exit one menu out, |  |  |  | 05: Bitstream |
|  |  | go from Zone to Main |  |  |  | 06: All DTS formats |
|  | QS | Query status |  |  |  | 07: PCM Auto |
|  |  | 00 = top (idle) screen |  |  |  | 08: PCM (CD audio) |
|  |  | 01..99=inside a submenu |  |  |  | 09: PCM 8 ch |
|  | DEC | Decrement parameter |  |  |  | 0a: AC3 (Dolby Dig) |
| TRIG |  | Trigger Output |  |  |  | 0b: DTS |
|  | abc | a=trig1,b=trig2,c=trig3 |  |  |  | 0c: AAC MPEG4,MPEG2,iPhone, |
|  | 000 | All triggers Off |  |  |  | iPod,iPad,NintendoDSi, |
|  | 0 | Trigger Off |  |  |  | iTunes,DivX,PS3,PSP, |
|  | 1 | Trigger On |  |  |  | SonyWalk,phones,Wii. |
|  | * | Trigger No Change |  |  |  | 0d: MPEG(MP1 Layer1 and 2) |
|  | QS | Query Status |  |  |  | 0e: DTS12 (DVD IEC Type 12) |
|  |  |  |  |  |  | 0f: DTS13 (DVD IEC Type 13) |
| LFVL |  | Left Front Vol Trim |  |  |  | 10: DTS14 (Type 14) |
|  | UP | Up 1 step (0.5dB) |  |  |  | 11: DTS16 (Type 16) |
|  | DN | Down 1 step (0.5dB) |  |  |  | 12: WMP (WMA Pro) |
|  | xxxx | 0880..1120 |  |  |  | 13: MP3 |
|  |  | (-12.0..12.0dB) |  |  |  | 14: DSD1 (SACD 1bit) |
|  | QS | Query Status |  |  |  | 15: DSD2 |
|  |  |  |  |  |  | 16: DSD3 |
| RFVL |  | Right Front Vol Trim |  |  |  | 17: DDP (Dolby Digital+) |
|  | UP | Up 1 step (0.5dB) |  |  |  | 18: DTS HD or Master |
|  | DN | Down 1 step (0.5dB) |  |  |  | 19: Dolby TrueHD |
|  | xxxx | 0880..1120 |  |  |  | 1a: DXP (DTS Express) |
|  |  | (-12.0..12.0dB) |  |  |  |  |
|  | QS | Query Status |  | AFMT |  | Query Input Format |
|  |  |  |  |  |  | (Program Format) |
| CNVL |  | Centre Vol Trim |  |  | QS | Query, returns program format |
|  | UP | Up 1 step (0.5dB) |  |  |  | as 8 digit hexadecimal number: |
|  | DN | Down 1 step (0.5dB) |  |  |  | BIT0 - Left Front Channel |
|  | xxxx | 0880..1120 |  |  |  | BIT1 - Right Front Channel |
|  |  | (-12.0..12.0dB) |  |  |  | BIT2 - Center Front |
|  | QS | Query Status |  |  |  | BIT8 - Single Surround Ch |
|  |  |  |  |  |  | BIT9 - Dual Side Surround Ch |
| SBVL |  | Subwoofer Vol Trim |  |  |  | BIT10 - Single Back Channel |
|  | UP | Up 1 step (0.5dB) |  |  |  | BIT11 - Dual Back Channel |
|  | DN | Down 1 step (0.5dB) |  |  |  | BIT12 - Low Freq Effects Ch |
|  | xxxx | 0880..1120 |  |  |  | BIT13 - Dual Subwoof (not supp) |
|  |  | (-12.0..12.0dB) |  |  |  | BIT16 – Not Stereo Surr Encoded |
|  | QS | Query Status |  |  |  | BIT17 - Yes Stereo Surr Encoded |
|  |  |  |  |  |  | BIT18 - Not Back Surr Encoded |
| LSVL |  | Left Surr Vol Trim |  |  |  | BIT19 - Yes Back Surr Encoded |
|  | UP | Up 1 step (0.5dB) |  |  |  | BIT20 - Mono |
|  | DN | Down 1 step (0.5dB) |  |  |  | BIT21 - Dual Mono |
|  | xxxx | 0880..1120 |  |  |  | BIT24 – Karaoke (not supp) |
|  |  | (-12.0..12.0dB) |  |  |  |  |
|  | QS | Query Status |  | RATE |  | Query Input Sample Rate |
|  |  |  |  |  |  | (Frame Rate) |
| RSVL |  | Right Surr Vol Trim |  |  | QS | Query, returns sample rate |
|  | UP | Up 1 step (0.5dB) |  |  |  | in Hz (000000=unknown). |
|  | DN | Down 1 step (0.5dB) |  |  |  |  |
|  | xxxx | 0880..1120 |  | VFMT |  | Query Video Input Format |
|  |  | (-12.0..12.0dB) |  |  | QS | Query, returns video timing |
|  | QS | Query Status |  |  |  | and format code xx in hex. |
|  |  |  |  |  |  | See SP3_Video_format_cmds document. |
| LBVL |  | Left Back Vol Trim |  |  |  |  |
|  | UP | Up 1 step (0.5dB) |  | VCOL |  | Video color depth |
|  | DN | Down 1 step (0.5dB) |  |  | QS | query, response xx= |
|  | xxxx | 0880..1120 |  |  |  | 00: AUTO |
|  |  | (-12.0..12.0dB) |  |  |  | 08: 3x8 bit |
|  | QS | Query Status |  |  |  | 0a: 3x10 bit |
|  |  |  |  |  |  | 0c: 3x12 bit |
| RBVL |  | Right Back Vol Trim |  |  |  | 10: 3x16 bit |
|  | UP | Up 1 step (0.5dB) |  |  |  | fe: not applicable |
|  | DN | Down 1 step (0.5dB) |  |  |  | ff: unknown |
|  | xxxx | 0880..1120 |  |  |  |  |
|  |  | (-12.0..12.0dB) |  | VCPP |  | Copy protection status |
|  | QS | Query Status |  |  | QS | query, response xx= |
|  |  |  |  |  |  | 00: none |
| SPFR |  | Front Speakers Setup |  |  |  | 01: HDCP |
|  | 00 | Off (Not allowed) |  |  |  | 02: Macrovision |
|  | 01 | Small |  |  |  | 80: AUTO |
|  | 02 | Large |  |  |  | 81: ON |
|  | QS | Query Status |  |  |  | ff: unknown |
| SPCN |  | Centre Speaker Setup |  |  |  |  |
|  | 00 | Off |  | OUTP |  | Query Output Format |
|  | 01 | Small |  |  |  | (Listening Format) |
|  | 02 | Large |  |  | QS | query, returns listening |
|  | QS | Query Status |  |  |  | format as 3 chars: |
|  |  |  |  |  |  | n.w |
| SPSB |  | Subwoofer Setup |  |  |  | or as 7 char string: |
|  | 00 | Off |  |  |  | f/s/b.w |
|  | 01 | On (not in bypass) |  |  |  |  |
|  | 02 | On (also in bypass) |  | INFO |  | Query system info (works in standby!) |
|  | QS | Query Status |  |  | QS | Query, returns system data as a |
|  |  |  |  |  |  | block of chars terminated by <CR> |
| SPSR |  | Surr Speakers Setup |  |  |  | (typically <300 chars). |
|  | 00 | Off |  |  |  | The data block is split |
|  | 01 | Small |  |  |  | into 22 <LF> delimited |
|  | 02 | Large |  |  |  | text lines, as follows: |
|  | QS | Query Status |  |  |  |  |
|  |  |  |  |  |  | #10INFO<LF> |
| SPBK |  | Back Speakers Setup |  |  |  | 01:%8sPRODUCT NAME<LF> |
|  | 00 | Off |  |  |  | 02:%8dSERNUM<LF> |
|  | 01 | 1 Small |  |  |  | 03:%8dMANUFDATE<LF> |
|  | 02 | 2 Small |  |  |  | 04:%12sSOFTWARE REV <LF> |
|  | 03 | 1 Large |  |  |  | 05:%8sBOOTLOADER REV<LF> |
|  | 04 | 2 Large |  |  |  | 06:%8xDSPA ID<LF> |
|  | QS | Query Status |  |  |  | 07:%8xDSPA VER<LF> |
|  |  |  |  |  |  | 08:%8xDSPB ID<LF> |
| SPCF |  | Speaker Config |  |  |  | 09:%8xDSPB VER<LF> |
|  |  | (Fr/C/Sur/Back/Sub) |  |  |  | 10:%8xCPU PIC32 REV<LF> |
|  | 00 | no change or unknown |  |  |  | 11:%8xHDMI VER REL<LF> |
|  | 01 | S/S/S/S2/Y |  |  |  | 12:%8xKEYPROC PIC16<LF> |
|  | 02 | L/S/S/S2/N |  |  |  | 13:%8xETHERNET<LF> |
|  | 03 | L/L/L/L2/N |  |  |  | 14:%8xFLASH<LF> |
|  | 04 | L/N/N/N/N |  |  |  | 15:%8xEEPROM<LF> |
|  | 05 | L/L/L/L2/Y |  |  |  | 16:%8xVOLUMECHIP<LF> |
|  | 06 | L/L/S/S2/Y |  |  |  | 17:%8xUSBAUDIO<LF> |
|  | 07 | S/S/S/N/Y |  |  |  | 18:%8xZDAC<LF> |
|  | 08 | L/L/S/N/Y |  |  |  | 19:%18sMACADDR[18] <LF> |
|  | QS | Query Status |  |  |  | 20:%16sNETBIOSNAME[16] <LF> |
|  |  |  |  |  |  | 21:%4dMAINBOARD REV<LF> |
| XBAS |  | Extra Bass Setup |  |  |  | <CR> |
|  |  | (sub must be on and |  |  |  | Note: %8x means 8 char hex, |
|  |  | front=large only) |  |  |  | %8d means 8 char dec, |
|  | 00 | Off or not applicable |  |  |  | %NNs - NN char str. |
|  | 0000 | same as above |  |  |  |  |
|  | xxxx | 0800..1000 |  |  |  |  |
|  |  | (-20.0 .. 0.0dB) |  |  |  |  |
|  | QS | Query Status |  | ASAV |  | Set auto-save |
|  |  |  |  |  |  | or force save now |
| MDSL |  | Mode Select |  |  | 00 | OFF - any parameter changed |
|  | 00 | not applicable,ignore |  |  |  | will not be automatically |
|  | AN | Analog |  |  |  | saved in EEPROM. |
|  | DI | Digital |  |  |  | (will require ASAVSV |
|  | HD | HDMI |  |  |  | Command to save!) |
|  | BP | Bypass 2-Channel |  |  | 01 | Automatically saves all |
|  | QS | Query Status |  |  |  | Changed parameters(within |
|  |  |  |  |  |  | 2s). Will also force |
| DISP |  | Display brightness |  |  |  | saving of currently |
|  | ON | On |  |  |  | modified parameters. |
|  | OF | Off |  |  | SV | Forces save all modified |
|  | 01 | 25% Brightness |  |  |  | parameters, without |
|  | 02 | 50% Brightness |  |  |  | changing the auto save |
|  | 03 | 75% Brightness |  |  |  | status (ON or OFF) |
|  | 04 | 100% Brightness |  |  | QS | Query, return auto-save |
|  | L1 | Returns Line 1 |  |  |  | Status |
|  | L2 | Returns Line 2 |  |  |  |  |
|  | L3 | Returns Line 3 |  | AUFB |  | Set auto-feedback |
|  | L4 | Returns Line 4 |  |  | 00 | OFF - automatic response |
|  | QS | Query Status |  |  |  | on device status change |
|  |  |  |  |  |  | or button press actions |
| LMOD |  | Set Listening Mode |  |  |  | will not be broadcast |
|  |  | (Surround Effects) |  |  |  | (only the responses to |
|  |  | 2 ch. to 7.1 speakers |  |  |  | explicit commands) |
|  | 00 | No Effects (2ch pass-through) |  |  | 01 | Automatic response |
|  | 01 | Dolby Pro Logic |  |  |  | will always be sent. |
|  | 02 | Dolby PLII Music |  |  | QS | query, return the AUFB |
|  | 03 | Dolby PLII Movie |  |  |  | status. |
|  | 04 | DTS Neo:6 Music |  |  |  |  |
|  | 05 | DTS Neo:6 Cinema |  | ____ | xx.. | Comment, null command |
|  | 06 | Stereo7 (7.1 speakers) |  |  |  | Always ignored, use for |
|  | 07 | Party 7 (mono 7.1 spk) |  |  |  | comments in scripts (xx.. is an |
|  | 08 | Room Reverb: Hall |  |  |  | arbitrary ASCII string, |
|  | 09 | Room Reverb: Church |  |  |  | can be empty). No response! |
|  | 10 | Room Reverb:Stadium |  |  |  |  |
|  | 11 | Room Reverb: Club |  | QVOL |  | Set Main Volume Quick |
|  | 12 | Room Reverb: Theatre |  |  | xxxx | 0200..1120 in 0.1dB |
|  | 13 | Natural |  |  |  | units plus 1000 |
|  | 14 | Stereo7x (use 7.1 spk and matrix algorithm) |  |  |  | Range -80.0..+12.0dB |
|  | 15 | DTS Neo:6 Cinema3 (3.1 speakers) |  |  |  | Resolution 0.5dB, (no ramp) |
|  |  | 5.1 ch to 7.1 speakers |  |  | QS | Query Status |
|  | 21 | 5.1 pass-through |  |  |  |  |
|  | 22 | DolbyDig.EX 6.1Movie |  | XVOL |  | Set Zone Volume Quick |
|  | 23 | PLIIx EX 6.1 Music |  |  | xxxx | 0200..1120 in 0.1dB |
|  | 24 | PLIIx EX 7.1 Movie |  |  |  | units plus 1000 |
|  | 25 | PLIIx EX 7.1 Music |  |  |  | Range -80.0.. +12.0dB, |
|  | 26 | PLIIx EX AUTO |  |  |  | Resolution 0.5dB, (no ramp) |
|  |  | Downmixing Modes |  |  | QS | Query Status |
|  | SU | SURR (no downmix) |  |  |  |  |
|  | ST | STEREO (2.1 speakers) |  | EDID |  | Force re-EDID on HDMI |
|  | MN | MONO (2.1 speakers) |  |  |  | (no parameters, returns OK or |
|  |  |  |  |  |  | ?? if failed) |
|  | QS | Query Status |  |  |  |  |

-- END OF FILE --